## Slide 1: Field Development Plan & Frac Metric Automation
August 2025

## Slide 2: Presentation Overview
Field Development Planning (FDP) Workflow
FDP Algorithm
  Completable and Drilling Length Auto-Calculation
  UWI and Pad Auto-Naming
Dynamic FDP Dashboard
  Automated Bulk Well Design
  Example Applications
Realtime Frac Dashboard
  Post-stage Automated Pressure Analysis
  Frac Hit Analysis
Conclusion
Agenda

## Slide 3: FDP Workflow
Converting Raw Field Development Plan Shapefile’s into fully designed Future Wells.
Field Development Plan Automation
FDP Shapefile
250+ Planned Wells
Input:
FDP Shapefile
Manually Assign each well it’s UWI & Pad Location
Measure well lengths (drilling and completable)
Add Completion Parameters
Add Type Curves + CGR/WGR
Add Capital Costs
Output: Mosaic Entities Ready for Economic Evaluation
FDP Automation Algorithm
Dynamic Spotfire Dashboard
Conclusion: New FDP Automation workflow increases planning accuracy, reduces/removes redundant tasks and creates off the shelf entities for Budget and Long-Range Planning analyses
Old
New
Future wells fully created and designed in Mosaic.
Input
Output

## Slide 4: FDP Algorithm: Completable Length Calculation
1 – FDP Algorithm 1st Component
Code calculates the completable length for all wells in the raw shapefile in a single pass, identifying precise locations of the toe and heel utilizing geometric math. Removing the time-consuming measuring process.
Conclusion: Algorithm increases precision in planning by providing well-specific measurements for an entire field, in a matter of a seconds.
Code can compute ~25 wells/second.
Python Calculation Algorithm
Completable Length Shapefile & Excel Sheet
Raw FDP Shapefile
FDP Shapefile
Calculation Code
Auto-name Code
Dynamic Dashboard
Ready for Evaluation
Input
Output
Red overlay is completable
Accurate drill/completable lengths help obtain more accurate budget inputs for five year outlook

## Slide 5: FDP Algorithm: Auto-assignment of UWI & Pad Location
After the algorithm identifies the toe point and location of the pad, the code maps each well to their respective sections – removing the repetitive task of naming every well.
2 - FDP Algorithm 1st Component
Conclusion: Algorithm reduces time spent on well location assignment by ~99%.
FDP Shapefile
Calculation Code
Auto-name Code
Dynamic Dashboard
Ready for Evaluation
LSD Section Shapefile
FDP Shapefile
Python Auto-name Algorithm
Final Algorithm Sheet
(All values below are automated)

## Slide 6: FDP Dynamic Dashboard
Dynamic Spotfire dashboard houses many Python Scripts, used to specify well parameters in bulk - has fields to enter all parameters and the code handles the rest. One-click exports into evaluation software Mosaic (economics and reserves evaluation platform).
FDP Shapefile
Calculation Code
Auto-name Code
Dynamic Dashboard
Ready for Evaluation
FDP Dashboard
Completions Tab
Type Curves Tab
CGR & WGR Tab
Capital Costs Tab
Calculates total sand volume (used in royalties), stage count, etc.
Generates volume forecast parameters by sub-area, scales curves by completable length.
Creates a month-by-month ratio forecast.
Calculates drilling cost (by zone), and completions cost (based on sand calculated in the completions tab). Updates Gas Equip and Gathering Cost.
Conclusion: The dashboard automates processing and uses the auto-calculated drilling and completed lengths - key well parameters - reducing time while increasing field development plan accuracy.

## Slide 7: FDP Workflow – Applications
Gold Creek Infrastructure Planning
Field Development Planning
Workflow applied to assess the GC FDP for long-range volumetric planning through 2040, providing volume recommendations for hydraulic modeling. In collaboration with Aaron Shaw to deliver an accurate evaluation of the recommended gas-gathering system.
GORR Evaluation – Risked PV10
The new workflow enabled a precise evaluation of the Gold Creek sections, quantifying the change in Risked PV10 attributable to each section’s respective GORR. This was achieved using exact linear meterage measurements, ensuring accuracy in assessing the economic impact at a granular level.
Conclusion: The new FDP workflow delivers faster, more precise volumetric and economic analyses.
FDP Shapefile
Calculation Code
Auto-name Code
Dynamic Dashboard
Ready for Evaluation

## Slide 8: Frac Spotfire Dashboard
Frac Dashboards integrated with Python Code allow for efficient real-time monitoring to create data-driven improvements during operations. Used by team daily during operations in morning call.
Frac Dashboards Created:
PSN 16-33, ELM 12-05, BIL 10-29, PSN 07-31, ELM 12-01, GC 14-30, ELM 16-35, PSN 12-28 and PSS 02-36P2
Frac Planning and Sequencing created alongside.
Raw Pumping Data
Auto-run Python Scripts
1,000,000+ Datapoints/week
Realtime Spotfire Visualizations

## Slide 9: Post-Stage Pressure Analysis
Frac Spotfire Dashboard
Python code extracts the slope of the pressure 10 minutes before the next stage, alongside the pressure. A new automated metric that can be used to validate parent-child behavior, shown clearly on Gold Creek 14-30.
Well | Average Final Slope (-kPa/min) | Average Final Pressure (MPa)
A-Well | 12.7 | 24.3
B-Well | 13.6 | 24.2
C-Well | 17.4 | 22.5
D-Well | 14.1 | 23.6
Conclusion: C-Well (Child well) showed strong traits of depletion - identified by new automated metrics. With pressure decreasing 28% faster than non-child MNTN A Well (B-Well), as well as a relatively lower average final pressure.
The D-Well (MNTN B) showed similar child traits when comparing to the non-child MNTN B Well (A-Well)
Pressure depletes
28% faster

## Slide 10: Frac Hit Analysis
Gauge data monitoring with the dashboard allows for easy identification of frac hits, both through auto-detection and easy visual flagging. Showcased on BIL 10-29 parent well, identifying that majority of sizeable hits occurred from the B-Well (same zone), rather than the child-well.
Frac Spotfire Dashboard
Large Frac Hit Distribution
Conclusion: Identifying the pumping well with cleaned gauge data showcases the dashboard’s power to reveal reservoir dynamics, improve well-to-well communication insights, and optimize future zone selection. Helped inform 10-29 Phase 2 layout.
04-27 Gauge Data – Frac Hits Identified

## Slide 11: Additional Projects
Technical Data Analysis:
  ExpressFiber Dashboard, 07-31 Clearvision, BIR Darkvision Completions, Seismic Array (PSN 16-33 & GC 14-30)
Operations Planning
  Perforation Planning, Frac Design, Sequencing, Data Surveillance
Single-use Economic Analyses
  L-Block, GORR, Individual Sections
Data Archiving
  CGR Database, Legacy Flowback Model, Frac Gauge and Pumping Data
Conclusion
What’s Next
Back to school in September for last year of Software Engineering, graduation May 2026
  Some Courses Include: Capstone (Team Design), Scalable Data Analytics, Quantum Theory/Computation
Work part-time during school with NuVista